## Slide 1: Chapter 1: Introduction
https://fb.com/tailieudientucnItt ntroduction
1-8
Our goal:
get “feel” and terminology
more depth, detail
later in course
approach:
  use Internet as
example
Overview:
what’s the Internet?
what’s a protocol?
network edge; hosts, access net, physical media
network core: packet/circuit
switching, Internet structure
performance: loss, delay, throughput
security
protocol layers, service models
history
CuuDuongThanCong.com

## Slide 2: Chapter 1: roadmap
  What is the Internet?
  Network edge
    end systems, access networks, links
  Network core
    circuit switching, packet switching, network structure
  Delay, loss and throughput in packet-switched
networks
  Protocol layers, service models
  Networks under attack: security
  History
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 3: What’s the Internet: “nuts and bolts” view
millions of connected computing devices: hosts = end systems
  running network
apps
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
fiber, copper, radio, satellite
transmission
rate = bandwidth
routers: forward
packets (chunks of data)
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 4: “Cool” internet appliances
World’s smallest web server
http://www-ccs.cs.umass.edu/~shri/iPic.html
IP picture frame http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 5: What’s the Internet: “nuts and bolts” view
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype,
Ethernet
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 6: What’s the Internet: a service view
communication infrastructure enables distributed applications:
  Web, VoIP, email, games,
e-commerce, file sharing
communication services provided to apps:
  reliable data delivery from source to destination
  “best effort” (unreliable) data delivery
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 7: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network
entities, and actions taken on msg transmission, receipt
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 8: What’s a protocol?
a human protocol and a computer network protocol:
Q: Other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection request
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 9: Chapter 1: roadmap
  What is the Internet?
  Network edge
    end systems, access networks, links
  Network core
    circuit switching, packet switching, network structure
  Delay, loss and throughput in packet-switched
networks
  Protocol layers, service models
  Networks under attack: security
  History
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 10: A closer look at network structure:
Introduction
1-17
network edge:
applications and hosts
access networks, physical media:
wired, wireless communication links
network core:
  interconnected routers
  network of networks
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 11: The network edge:
end systems (hosts):
  run application programs
  e.g. Web, email
client/server
peer-peer
at “edge of network”
client/server model
client host requests, receives service from always-on server
e.g. Web browser/server;
email client/server
peer-peer model:
  minimal (or no) use of dedicated servers
  e.g. Skype, BitTorrent
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 12: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 13: Dial-up Modem
telephone network
Internet
home dial-up modem
ISP
modem (e.g., AOL)
home PC
central
office
Uses existing telephony infrastructure
  Home is connected to central office
up to 56Kbps direct access to router (often less)
Can’t surf and phone at same time: not “always on”
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 14: Digital Subscriber Line (DSL)
telephone network
DSL
modem
home PC
home phone
Internet
DSLAM
Existing phone line:
0-4KHz phone; 4-50KHz upstream data; 50KHz-1MHz downstream data
splitter
central office
Also uses existing telephone infrastruture
up to 1 Mbps upstream (today typically < 256 kbps)
up to 8 Mbps downstream (today typically < 1 Mbps)
dedicated physical line to telephone central office
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 15: Residential access: cable modems
https://fb.com/tailieudientucnItt ntroduction
1-22
Does not use telephone infrastructure
  Instead uses cable TV infrastructure
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream, 2 Mbps upstream
network of cable and fiber attaches homes to ISP router
  homes share access to router
  unlike DSL, which has dedicated access
CuuDuongThanCong.com

## Slide 16: Residential access: cable modems
Introduction
1-23
Diagram: http://www.cabledatacomnews.com/cmic/diagram.html
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 17: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)
Typically 500 to 5,000 homes
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 18: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
server(s)
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 19: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 20: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
Channels
 |  |  |  |  |  |  |  | C
 |  |  |  |  |  |  |  | O
V | V | V | V | V | V |  |  | N
I | I | I | I | I | I | D | D | T
D | D | D | D | D | D | A | A | R
E | E | E | E | E | E | T | T | O
O | O | O | O | O | O | A | A | L
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
FDM (more shortly):
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 21: Fiber to the Home
ONT | 
OLT
central office
optical splitter
ONT | 
ONT | 
optical
fiber
optical fibers
Internet
Optical links from central office to the home
Two competing optical technologies:
  Passive Optical network (PON)
  Active Optical Network (PAN)
Much higher Internet rates; fiber also carries television and phone services
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 22: Ethernet Internet access
100 Mbps
100 Mbps
Ethernet
switch
Institutional
router
1 Gbps
100 Mbps
server
Typically used in companies, universities, etc
10 Mbs, 100Mbps, 1Gbps, 10Gbps Ethernet
Today, end systems typically connect into Ethernet switch
To Institution’s
ISP
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 23: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access
point”
wireless LANs:
  802.11b/g (WiFi): 11 or 54 Mbps
wider-area wireless access
  provided by telco operator
  ~1Mbps over cellular system (EVDO, HSDPA)
  next up (?): WiMAX (10’s Mbps)
over wide area
base
station
mobile hosts
router
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 24: Home networks
Typical home network components:
DSL or cable modem
router/firewall/NAT
Ethernet
wireless access point
wireless access point
wireless
laptops
router/
firewall
cable modem
to/from cable headend
Ethernet
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 25: Physical Media
Bit: propagates between transmitter/rcvr pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely,
e.g., radio
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5: 100Mbps Ethernet
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 26: Physical Media: coax, fiber
Coaxial cable:
two concentric copper conductors
bidirectional
baseband:
  single channel on cable
  legacy Ethernet
broadband:
  multiple channels on cable
  HFC
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s- 100’s Gps)
low error rate: repeaters spaced far apart ; immune to electromagnetic noise
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 27: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., Wifi)
  11Mbps, 54 Mbps
wide-area (e.g., cellular)
  3G cellular: ~ 1 Mbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low
altitude
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 28: Chapter 1: roadmap
  What is the Internet?
  Network edge
    end systems, access networks, links
  Network core
    circuit switching, packet switching, network structure
  Delay, loss and throughput in packet-switched
networks
  Protocol layers, service models
  Networks under attack: security
  History
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 29: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in
discrete “chunks”
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 30: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 31: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 32: Circuit Switching: FDM and TDM
https://fb.com/tailieudientucnItt ntroduction
1-39
FDM
frequency
time
TDM
frequency
time
4 users
Example:
CuuDuongThanCong.com

## Slide 33: Numerical example
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit
Let’s work it out!
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 34: Network Core: Packet Switching
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  Node receives complete
packet before forwarding
each end-end data stream divided into packets
user A, B packets share
network resources
each packet uses full link bandwidth
resources used as needed
Bandwidth division into “pieces” Dedicated allocation Resource reservation
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 35: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern, bandwidth shared on demand  statistical multiplexing.
TDM: each host gets same slot in revolving TDM frame.
A
B
C
100 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets waiting for output link
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 36: Packet-switching: store-and-forward
entire packet must arrive at router before it can be transmitted on next link
delay = 3L/R (assuming zero propagation delay)
R
takes L/R seconds to transmit (push out) packet of L bits on to link at R bps
store and forward:
R
R
Example:
L = 7.5 Mbits
R = 1.5 Mbps
transmission delay = 15 sec
L
more on delay shortly …
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 37: Packet switching versus circuit switching
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
Packet switching allows more users to use network!
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
N users
1 Mbps link
Q: how did we get value 0.0004?
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 38: Packet switching versus circuit switching
Introduction 1-45
Is packet switching a “slam dunk winner?”
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion: packet delay and loss
  protocols needed for reliable data transfer,
congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
Q: human analogies of reserved resources (circuit
switching) versus on-demand allocation (packet-switching)?
CuuDuongThanCong.com https://fb.com/tailieudientucntt

## Slide 39: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., Verizon, Sprint, AT&T, Cable and Wireless), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 40: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
…
.
…
…
…
POP: point-of-presence
to/from backbone
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 41: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier 1 ISP
Tier-2 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of tier-1 provider
Tier-2 ISPs also peer privately with each other.
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 42: Internet structure: network of networks
Introduction
1-49
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier-2 ISP
local
ISP
local ISP
local ISP
local ISP
local
ISP
Tier 3
ISP
Tier-2 ISP
Tier 1 ISP
Tier-2 ISP
local ISP
Tier 1 ISP
Tier-2 ISP local ISP
Tier-2 ISP
local
ISP
Local and tier- 3 ISPs are customers of higher tier ISPs
connecting them to rest of Internet
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 43: Internet structure: network of networks
Introduction
1-50
a packet passes through many networks!
Tier 1 ISP
Tier-2 ISP
local
ISP
local ISP
local ISP
local ISP
local
ISP
Tier 3
ISP
Tier-2 ISP
Tier 1 ISP
Tier-2 ISP
local ISP
Tier 1 ISP
Tier-2 ISP local ISP
Tier-2 ISP
local
ISP
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 44: Chapter 1: roadmap
https://fb.com/tailieudientucnItt ntroduction
1-51
  What is the Internet?
  Network edge
    end systems, access networks, links
  Network core
    circuit switching, packet switching, network structure
  Delay, loss and throughput in packet-switched
networks
  Protocol layers, service models
  Networks under attack: security
  History
CuuDuongThanCong.com

## Slide 45: How do loss and delay occur?
Introduction
1-52
B
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
packet being transmitted (delay)
A
packets queueing (delay)
free (available) buffers: arriving packets dropped (loss) if no free buffers
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 46: Four sources of packet delay
https://fb.com/tailieudientucnItt ntroduction
1-53
1. nodal processing:
  check bit errors
  determine output link
A
B
propagation
transmission
nodal processing
queueing
2. queueing
  time waiting at output link for transmission
  depends on congestion level of router
CuuDuongThanCong.com

## Slide 47: Delay in packet-switched networks
Introduction
1-54
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal processing
queueing
Note: s and R are very
different quantities!
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 48: Caravan analogy
cars “propagate” at
100 km/hr
toll booth takes 12 sec to service car (transmission time)
car~bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
toll booth
Time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
Time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll booth
ten-car caravan
100 km 100 km
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 49: Caravan analogy (more)
Cars now “propagate” at 1000 km/hr
Toll booth now takes 1 min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at 1st booth?
toll booth
Yes! After 7 min, 1st car at 2nd booth and 3 cars still at 1st booth.
1st bit of packet can arrive at 2nd router before packet is fully transmitted at 1st router!
  See Ethernet applet at AWL Web site
toll booth
ten-car caravan
100 km 100 km
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 50: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
 = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs
dnodal  dproc  dqueue  dtrans  dprop
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 51: Queueing delay (revisited)
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 52: “Real” Internet delays and routes
1-59
What do “real” Internet delay & loss look like?

Traceroute
program: provides delay
measurement from source to router along end-end Internet path towards destination. For all i:
sends three packets that will reach router i on path towards destination
router i will return packets to sender
sender times interval between transmission and reply.
3 probes
probes
https://fb.com/tailieudientucnItt ntroduction

## Slide 53: “Real” Internet delays and routes
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from gaia.cs.umass.edu to cs-gw.cs.umass.edu
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
* means no response (probe lost, router not replying)
trans-oceanic link
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 54: Packet loss
A
B
packet being transmitted
packet arriving to full buffer is lost
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
buffer
(waiting area)
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 55: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with file of F bits to send to clien
link capacity Rs bits/sec
t
link capacity Rc bits/sec
pipe that can carry fluid at rate
Rs bits/sec)
pipe that can carry fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 56: Throughput (more)
Rs < Rc
What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc
What is average end-end throughput?
Rs bits/sec
Rc bits/sec
bottleneck link
link on end-end path that constrains end-end throughput
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 57: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 58: Chapter 1: roadmap
  What is the Internet?
  Network edge
    end systems, access networks, links
  Network core
    circuit switching, packet switching, network structure
  Delay, loss and throughput in packet-switched
networks
  Protocol layers, service models
  Networks under attack: security
  History
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 59: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of
organizing structure of network?
Or at least our discussion
of networks?
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 60: Organization of air travel
ticket (purchase)
baggage (check)
gates (load) runway takeoff airplane routing
ticket (complain)
baggage (claim) gates (unload) runway landing airplane routing
airplane routing
a series of steps
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 61: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure airport
arrival airport
airplane routing airplane routing
intermediate air-traffic
control centers
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
Layers: each layer implements a service
via its own internal-layer actions
relying on services provided by layer below
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 62: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 63: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data
transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport network link physical
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 64: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine- specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these
layers!
  these services, if needed, must be implemented in application
  needed?
application presentation session transport network
link physical
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 65: Encapsulation
source
application
transport
network link
physical
Hn
Ht M
segment
Ht
datagram
destination
application
transport
network
link
physical
 | Hn | Ht | M
Hl | Hn | Ht | M
Ht
M
M
network
link
physical
Hl Hn Ht M
Hn | Ht | M
Hn
Ht M
Hn Ht
Hl
M
router
link physical
switch
message
M
Ht
M
Hn
frame
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 66: Chapter 1: roadmap
  What is the Internet?
  Network edge
    end systems, access networks, links
  Network core
    circuit switching, packet switching, network structure
  Delay, loss and throughput in packet-switched
networks
  Protocol layers, service models
  Networks under attack: security
  History
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 67: Network Security
The field of network security is about:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  Security considerations in all layers!
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 68: Bad guys can put malware into hosts via Internet
Malware can get in host from a virus, worm, or
trojan horse.
Spyware malware can record keystrokes, web sites visited, upload info to collection site.
Infected host can be enrolled in a botnet, used for spam and DDoS attacks.
Malware is often self-replicating: from an infected host, seeks entry into other hosts
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 69: Bad guys can put malware into hosts via Internet
Introduction
1-76
Trojan horse
  Hidden part of some otherwise useful software
  Today often on a Web page (Active-X, plugin)
Virus
  infection by receiving object (e.g., e-mail attachment), actively executing
  self-replicating: propagate itself to other hosts, users
Worm:
  infection by passively receiving object that gets itself executed
  self- replicating: propagates to other hosts, users
Sapphire Worm: aggregate scans/sec
in first 5 minutes of outbreak (CAIDA, UWisc data)
CuuDuongThanCong.com
https://fb.com/tailieudientucntt

## Slide 70: Bad guys can attack servers and network infrastructure
Denial of service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
select target
break into hosts around the network (see botnet)
send packets toward
target from compromised hosts
target
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 71: The bad guys can sniff packets
Packet sniffing:
broadcast media (shared Ethernet, wireless)
promiscuous network interface reads/records all
packets (e.g., including passwords!) passing by
A
C
src:B dest:A
payload
B
Wireshark software used for end-of-chapter labs is a (free) packet-sniffer
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 72: The bad guys can use false source addresses
IP spoofing: send packet with false source address
A
B
C
src:B
dest:A
payload
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 73: The bad guys can record and playback
B
record-and-playback: sniff sensitive info (e.g.,
password), and use later
  password holder is that user from system point of view
C
A
src:B dest:A
user: B; password: foo
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 74: Network Security
more throughout this course
chapter 8: focus on security
crypographic techniques: obvious uses and not so obvious uses
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 75: Chapter 1: roadmap
  What is the Internet?
  Network edge
    end systems, access networks, links
  Network core
    circuit switching, packet switching, network structure
  Delay, loss and throughput in packet-switched
networks
  Protocol layers, service models
  Networks under attack: security
  History
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 76: Internet History
1961: Kleinrock - queueing theory shows effectiveness of packet- switching
1964: Baran - packet- switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demonstration
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 77: Internet History
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
ate70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking
principles:
minimalism, autonomy - no internal changes required to interconnect networks
best effort service model
stateless routers
decentralized control define today’s Internet
architecture
1972-1980: Internetworking, new and proprietary nets
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 78: Internet History
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP- address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 79: Internet History
decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s:
commercialization of the Web
Late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to
forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps
Early 1990’s: ARPAnet
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 80: Internet History
2007:
~500 million hosts
Voice, Video over IP
P2P applications: BitTorrent (file sharing) Skype (VoIP), PPLive (video)
more applications: YouTube, gaming
wireless, mobility
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com

## Slide 81: Introduction: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
security
history
You now have:
context, overview,
“feel” of networking
more depth, detail to follow!
https://fb.com/tailieudientucnItt ntroduction
CuuDuongThanCong.com